Vocare LEDlight

SPECIFICATION

BRAND        :    Vocare LED light

DESCRIPTION  : LED PANEL LIGHT

MODEL NO     : Vocare-02-48W

Web: www.vocare-ledlight.com

Contact: sales@vocare-ledlight.com

Photo of product

- Features

  - Energy saved up to 70%.

  - Slim and practical, with 12mm thickness and excellent brightness

  - Superb even light distribution, with no dark zone or white spot

  - Unique outer frame design and special durable driver

  - Special different view angles, mixing lighting design

  - Instant start, no flickering, no humming

  - New inner high efficiency (95%) With heat protection

  - The constant current driver can work under unstable voltage.

  - Special circuit design,each LED can work separately, avoid the influnence that a broken LED causes.

  - No electric wave.and No RF interference

  - No such hazard that mercury of lead enters the environment

- Technical Parameters

| Model Number | JDL-02-48W |
| --- | --- |
| Power | 48W |
| Measurement | 600*600*12mm |
| LED Amount | 96PCS |
| LED Type | 5630 |
| Input Voltage | AC95V~AC265V 50Hz/60Hz |
| Power Factor | ≥0.85 |
| Light Color | Warm white,white |
| Light Decay | Less than 3% after 10000hours constant work |
| Ra | Ra≥70 |
| Color temperature | 3000K-6500K |
| Luminous Flux | 3000-3100 lumens Warm white;3200-3300 lumens white |
| Lifespan | ≥50000 Hours |
| Beam Angle | 120 Degrees |
| Material | Al |
| Working Environment | -40°C~80°C |
| Working Humidity | ≤95% |
| Storage condition | -40°C~80°C |
| Product Standard | CE certificated and RoHS compliant |

- LEDs Lumen Attenuation:

| Operating time(hours) | Lumen decrease(%) |
| --- | --- |
| 5,000 | 2 |
| 10,000 | 3 |
| 20,000 | 8 |
| 50,000 | 12 |

- Product Dimensions:

Notes:

1. All dimension units are millimeters.

2. All dimension tolerance is ±0.5mm unless otherwise noted.

- Package

Measurement:  L700*W700*H270mm（4pcs/carton）

- Electrical connection:

1.Before starting the connection, make sure the power supply is switched off.

2.Connect the driver DC output end to the panel DC input end.

3.Wire the AC power supply to the driver AC input end properly. Make sure all connections are firm and correct.

4.Switch on the power supply to turn on the light.

- Installation instructions:

- Products Application Cases

  - Hotels

  - Conference/Meeting rooms

  - Factories & Offices

  - Commercial complex

  - Airports and metro stations

  - Commercial Purposes.

  - Residential/Institution Buildings

  - Schools,Colleges ,Universities,Hospitals